DATE:   29 March, 1993                             File No. TBC93-6

Technical Bulletin

RE:	Mounting info for Marquee 8000 and 9000.

There has been numerous request for information in regards to specifications for mounting of the Marquee Series projectors.  The following is a collection of literature which collectively should provide you with enough information to design an installation layout.

Specifications of the Electrohome Ceiling mount is included and highly recommended because of its pulley system.  Although there is nothing wrong with using a simple plate and bolt system, it has been our experience that physically lifting a projector of this weight and shape without mechanical assistant is very dangerous.  This fact is made worse because of the curved nature of the projector covers.  It is also important to note that the projector's case covers were not designed to support the weight of the projector.  This is particularly tricky at the front of the projector where all the weight resides.

If an Electrohome mount is not used, an alternative method of lifting the projector other than 4 pairs of hands is needed.  Please also ensure that any materials mounted directly onto the projector be made of a non-magnetic material like aluminum.

All external mechanical dimensions for the Marquee 8000 and 9000 are the same.  The only difference is weight.  However the small weight difference should not be considered since a proper mounting system should be capable of several hundred pounds.

1